## Slide 1
Minimally Invasive Solution for Prolapse repair

## Slide 2
Single incision mesh for vaginal prolapse correction
For anterior, posterior and apical prolapse correction without needles
Fixed to the sacrospinous ligament with Anchorsure
Fixed to the internal obturator muscle by “pockets” (fibrosis)
WHAT IS IT?

## Slide 3
COMPLETE SYSTEM
Anchorsure
Mesh
Free needle

## Slide 4
The Mesh
Material: Macropore polypropylene monofilament
Density: 28g/m2 - ultralight
AMID Classification: Type I (pore >70µm)
Tensile strength break: 40N/cm

## Slide 5
MIPS offers versatility and can be adapted to any vaginal prolapse type. Depending on the prolapse location it will be used:
2 arms “pockets”: anterior and apical prolapse
    The mesh in placed between the bladder and the vagina
    It is a single incision mesh since only one incision is made in the vagina to place it (without needles)
The mesh

## Slide 6
Without arms: posterior and apical prolapse
  The mesh is placed between the vagina and the rectus

## Slide 7
Posterior fixation: to the sacrospinous ligament with Anchorsure
Anterior fixation: to the internal obturator muscle. Fixation will be achieved by fibrosis of the tissue
1
2
1
2
FIXATION POINTS

## Slide 8
Anterior arms or “pockets” are fixed inside the internal obturator muscle with a “Koher” type forceps in the 2 and 10 o’clock position.
The “pockets” offer a short term mechanical fixation but at mid and long term, fixation will be achieved by fibrosis.
The thread indicates the center of the mesh.
ARMS USE

## Slide 9
Ultralight and big pore mesh
Minimally invasive solution for vaginal prolapse repair
Total mesh adjustability to reduce erosion and extrusion
Maximum versatility: same mesh for any compartment
Trimmable and adaptable mesh
Sacrospinous ligament fixation by Anchorsure
SUMMARY ADVANTATGES AND BENEFITS

## Slide 10
NECESSARY MATERIAL FOR SURGERY
KITMIPS02: Complete kit with single use sterile instruments

## Slide 11
SURGICAL TECHNIQUE

## Slide 12
If the complete kit is not used, the applicator APLIC 01 must be sterilized
Follow indications on the Anchorsure placement.
Important. Reminder on how to hold the mesh pocket with the forceps, and the forceps with the palm of your hand.
Important. Push the mesh with the forceps well into the inner obturator muscle on the right side until the blue central thread has passed the urethra more than 1 cm. on that side. When placing the left side pocket, push the forceps well into the internal obturator muscle until the central thread is centered below the urethra.
REMINDER FOR OPERATING ROOM

## Slide 13
Vídeos
1. Promedon - Calistar A / P / S
2. AMI - InGYNious
3. Coloplast - Restorelle
COMPETETITION

## Slide 14
BENEFITS AGAINST OTHER MESHES / SYSTEMS
  Single incision mesh (less invasive, less groin pain)
  Mesh adjustability: prevents wrinkle formation
  Versatility: same mesh for any prolapse
  All the advantages offered by Anchorsure compared to other sacrospinous ligament fixation systems
HEALTHCARE PROFESSIONALS BENEFITS

## Slide 15
Producto
Less invasive as it is a single incision mesh
Allows adaptability to decrease risk of erosions
PATIENT’S BENEFITS

## Slide 16
Vídeos
Materiales
MIPS
KEY MESSAGES
Single incision mesh: less risk of groin pain
Versatility: for any type of prolapse
Adjustability: reduces erosion risk
Sacrospinous ligament fixation with anchors: reduces risk of vaginal shortening

## Slide 17
THANK YOU